## Slide 1
Health and safety legislation
Unit 201: Health and safety in building services engineering

## Slide 2: Definitions
Employer – A person or body that employs one or more persons under a contract of employment.
Employee – A person employed by an employer under a contract of employment.
Organisations – An organisation is an entity comprising multiple people, such as an institution or an association, that has a collective goal and is linked to an external environment.
Clients – a person or organisation using the services of the company. In other words, the customer.
Statutory – This means that it is binding in law and is a criminal act to contravene it.
Non-statutory – Not legally binding. However, many non‑statutory regulations are based on statutory ones so breaking them could mean that a law may have been broken somewhere.

## Slide 3: Health and Safety at Work etc Act
This covers all places where work is carried out. The ‘etc’ was added to cover voluntary work, etc. All persons are responsible for their own and others’ safety.
Employers’ responsibilities
The working conditions and standards of hygiene are appropriate.
The plant, tools and equipment are properly maintained.
The necessary safety equipment – such as personal protective equipment, dust and fume extractors, and machine guards – is available and properly used.
The workers are trained to use the equipment and plant safely.

## Slide 4: Health and Safety at Work etc Act
This covers all places where work is carried out. The ‘etc’ was added to cover voluntary work, etc. All persons are responsible for their own and others’ safety.
Employees’ responsibilities
Take reasonable care to avoid injury to themselves or others as a result of their own work activity.
Cooperate with their employer, helping her/him to comply with the requirements of the Act.
Not to interfere with or misuse anything provided to protect their health and safety.

## Slide 5: The Electricity at Work Regulations
Currently 33 regulations.
1–16 and 29 most relevant to electricians.
This is a legal (statutory) document.
Wiring regulations (BS 7671) are not.

## Slide 6: Management of Health and Safety at Work Regulations
Places duties on employers and employees including those who are clients, designers, principal contractors or other contractors.
Many of the duties overlap with those of CDM but where they go beyond CDM (for example concerning young people and expectant mothers) additional measures will be needed to comply fully with MHSWR.

## Slide 7: Workplace (Health and Safety and Welfare) Regulations
People in control of non-domestic premises have a duty towards people who are not their employees but use their premises. The Regulations expand on these duties and are intended to protect the health and safety of everyone in the workplace, and ensure that adequate welfare facilities are provided for people at work.
The Regulations aim to ensure that workplaces meet the health, safety and welfare needs of all members of a workforce, including people with disabilities. Workstations should be made accessible for disabled people.

## Slide 8: Control of Substances Hazardous to Health (COSHH) Regulations
Covers anything used in the workplace that could be considered hazardous to health.
Includes chemicals, asbestos, cements, oils, sprays, etc.

## Slide 9: Working at Height Regulations
More people are killed and injured by falls than any other cause.
This document summarises what you need to do to comply with the Work at Height Regulations 2005.

## Slide 10: Personal Protective Equipment (PPE) at Work Regulations
Requires an assessment of PPE requirements to be carried out.
Employer to supply the PPE.
Employee to wear the protective equipment.

## Slide 11: Manual Handling Operations Regulations
Aim to reduce the very large incidence of injury and ill health caused by the manual handling of loads at work.

## Slide 12: Provision and Use of Work Equipment Regulations
Covers the supply and use of equipment in the workplace.
Equipment must be safe to use and used safely by the operatives.

## Slide 13: Control of asbestos at Work Regulations
The name again clearly explains the coverage of the regulations.
Asbestos is an extremely dangerous material when disturbed and any possible exposure to or presence of asbestos should be reported immediately.

## Slide 14: Environmental Protection Act
The EPA is an Act defines, within England and Wales and Scotland, the fundamental structure and authority for waste management and control of emissions into the environment.

## Slide 15: Hazardous Waste Regulations
These regulations have been introduced to control the storage, transport and disposal of hazardous waste to ensure it is appropriately managed and any risks are limited.

## Slide 16: Pollution Prevention and Control Act
Under this new Act, Local Authorities are required to regulate the smaller industries termed Part A2 and Part B installations. Whereas the Environment Agency regulates the larger industries, which are known as Part A1 installations.
Emissions to all environmental media must be controlled from Part A1 and A2 installations and such installations are also required to account for energy efficiency and to control against Noise Pollution. Part B installations on the other hand are regulated for emissions to air only.

## Slide 17: Control of Pollution Act
The aim of the Act is to deal with a variety of environmental issues, including waste on land, water pollution, abandoned mines, noise pollution and the prevention of atmospheric pollution.

## Slide 18: The Control of Noise at Work Regulations
These regulations place a duty on employers to reduce the risk to their employees’ health by controlling the noise they are exposed to whilst at work

## Slide 19: The Waste Electrical and Electronic Equipment Regulations (WEEE)
These regulations regulate the management of electrical and electronic waste.
A key objective of the WEEE Regulations is to reduce the amount of WEEE that goes to landfills.
This is achieved by placing an extended responsibility on producers and distributors of electrical and electronic equipment. Under the extended responsibility obligations, producers are required to finance the collection, treatment and recovery of WEEE.
The WEEE Regulations also place an obligation on distributors to offer to consumers a take-back system where WEEE items can be disposed of free of charge.
There are two types of take-back systems, and distributors of EEE items must offer one of these schemes to their customers.

## Slide 20
The End
Unit 201: Health and safety in building services engineering