## Slide 1
Hazards
Unit 201: Health and safety in building services engineering

## Slide 2: Definitions
A Hazard is a potential source of harm or adverse health effect on a person or persons
Risk is the likelihood that a person may be harmed or suffers adverse health effects if exposed to a hazard

## Slide 3: Specific hazards
There are specific hazards that operatives associated with the installation and maintenance of electrical systems and equipment including the following:
Electric shock (direct and indirect contact)
Burns
Fires
Explosions

## Slide 4: Electric shock
An electric shock can be defined as:
The physiological reaction, sensation, or injury caused by electric current passing through the (human) body.
The direct danger is the damage that the power itself can do to the human body, such as stoppage of breathing or regular heartbeats, or burns.
The indirect dangers of electricity include the damages that can result to the human body as a result of something caused by electric shock, such as a fall, an explosion or a fire.

## Slide 5: Electric shock
Contact with live parts is referred to as ‘Direct Contact’.
When an electric shock is received from conductive parts that should not normally be live it is referred to as ‘Indirect contact’, occurring when there is a fault; for example exposed conductive parts and extraneous conductive parts.
The International Electrotechnical Commission (IEC) requires certain degrees of ingress protection against direct contact.
Indirect contact protection can be achieved by earthed equipotential bonding and automatic disconnection of supply by using Residual Current Devices (RCDs).

## Slide 6: Burns
Being exposed to electric shock not only has an effect on the nervous system and muscles of the body but can also result in burns.
What makes electrical burns even more dangerous is that they may not necessarily be visible on the surface of the body.

## Slide 7: Fires
If a short circuit occurs in an electrical circuit due usually to a fault, resulting sparks could ignite flammable materials and gases in the vicinity.
To this end the electrical regulations, BS7671, contains a chapter entitled, ‘Protection Against Fire’. Protection against fire resulting from the electrical installation and the use of the electrical installation has been necessary ever since electricity was introduced into buildings.

## Slide 8: Explosions
If the installation has a potentially explosive atmosphere sparks produced by the electrical installation, whether as a result of a fault or during normal operation (e.g. spark when contact carrying current opens), could ignite this explosive atmosphere.
An explosive atmosphere can be defined as a mixture of dangerous substances with air, under atmospheric conditions, in the form of gases, vapours, mist or dust in which, after ignition has occurred, combustion spreads to the entire unburned mixture.

## Slide 9: Explosions
When installing or maintaining electrical equipment in areas containing an explosive atmospheres special care must be taken to ensure that an sparks produced by the electrical installation cannot ignite the explosive atmosphere. This is referred to as ‘Intrinsically Safe’. This can be defined as:
Intrinsically safe equipment and wiring shall not be capable of releasing sufficient electrical or thermal energy under normal or abnormal conditions to cause ignition of a flammable or combustible atmospheric mixture in its most easily ignitable concentration.

## Slide 10
The End
Unit 201: Health and safety in building services engineering