## Slide 1
Firefighting procedures
Unit 201: Health and safety in building services engineering

## Slide 2: Fire and firefighting
OXYGEN: all fires need a supply of oxygen to burn.
Smother a fire by isolating the fire from the supply of oxygen.
HEAT: a naked flame, match or spark is sufficient to start a fire, especially if in contact with something which is flammable.
Cool a fire by using water to lower the temperature.
FUEL: can be anything that will burn, eg wood, furniture, flammable liquid, gas, etc.
Starve a fire by removing fuel.
FIRE TRIANGLE

## Slide 3: Fire and firefighting
If you discover a fire:
raise the alarm
close doors and windows to prevent fire spreading
evacuate the area
fight the fire with an extinguisher, fire blanket, water or sand, only if you have been trained to do so
never put your own safety at risk.

## Slide 4: Fire and firefighting
Firefighting should not continue if:
the fire becomes too dangerous
there is a possibility that any escape route might be cut off
the fire continues to spread and becomes out of control
there are gas cylinders or other highly flammable materials in the immediate fire area that cannot be removed or protected.

## Slide 5: Classification of fires
Fires involving wood, paper, textiles and other carbonaceous materials.
Fires involving flammable liquids, petrol and spirits.
Fires involving flammable gases, eg propane and butane.
Fires involving burning metals, eg aluminium, magnesium (where water is generally ineffective and/or dangerous).
Electrical fires are not considered to constitute a fire class of their own, as electricity is a source of ignition that will feed a fire until removed.
Fires involving cooking oil and fat, eg olive oil, maize oil, lard and butter.

## Slide 6: Fire extinguishers
When using flammable materials, a suitable fire extinguisher must always be kept handy and ready for use.
Make sure that the extinguisher is the right type for the fire that may occur.
Before starting work on any job, make sure that the extinguisher’s operating instructions are fully understood.
Fire extinguishers are colour coded for easy recognition and you should familiarise yourself with the codes and their uses.

## Slide 7: Fire extinguishers
Old colour BS5406 | New colour BS EN3 | Class A paper or wood, etc | Class B flammable liquids | Class C flammable gas fires | Class D metal fires | Electrical fires
Note: Multi-purpose Foams may be used
Note: Specialist Foams required for industrial alcohol

## Slide 8: Fire extinguishers
Old colour BS5406 | New colour BS EN3 | Class A paper or wood, etc | Class B flammable liquids | Class C flammable gas fires | Class D metal fires | Electrical fires
General Note – May be used in conjunction with other extinguishing agents or fire extinguishing techniques.
SPECIALIST HOT COOKING OIL FIRES ONLY
Specifically for dealing with high temperature (360°C+) cooking oils used in large industrial size catering kitchens, restaurants and takeaway establishments with deep fat frying facilities.
Note: Specialist DP required for Solvents & Esters
Note: Specialist Dry Powders may be required

## Slide 9
The End
Unit 201: Health and safety in building services engineering