## Slide 1
Resistors in series
Unit 202: Principles of electrical science

## Slide 2
RT = R1 + R2 + R3
Resistors in series

## Slide 3
Calculate the total resistance of the circuit shown below:
Example 1

## Slide 4
RT | = | R1 + R2 + R3 + R4
Calculate the total resistance of the circuit shown below:
Put some figures in:
Calculate through to give:
 | = | 18Ω
 | = | 2 + 5 + 8 + 3
Example 1

## Slide 5
RT | = | R1 + R2 + R3
Calculate the current that will flow in the circuit shown below:
Put some figures in:
Calculate through to give:
 | = | 2A
 | = | 2 + 3 + 7
Example 2

## Slide 6
Calculate the current that will flow in the circuit shown below:
Example 2

## Slide 7
Equivalent circuit:
I | = | V R
 | = | 24 12
 | = | 2A
Example 2

## Slide 8
V | = | I × R
What potential is produced across a resistance of 23 if a current of 10 amps is flowing through it?
Put some figures in:
Calculate through to give:
 | = | 230 volts
 | = | 10 × 23
Example 3

## Slide 9
The algebraic sum of the voltages around a circuit is equal to zero (or the supply voltage).
VS = V1 + V2 + V3
Kirchoff’s Voltage law

## Slide 10
RT | = | R1 + R2 + R3
Calculate V1, V2, V3, hence, proving Kirchhoff's Voltage law.
 | = | 3 + 5 + 7
 | = | 15Ω
I | = | V R
 | = | 90 15
 | = | 6A
Example 4

## Slide 11
 | = | 6 × 5
 | = | 30V
Resistor 2
V3 | = | I × R3
 | = | 6 × 7
 | = | 42V
Resistor 3
VT | = | V1 + V2 + V3
 | = | 18 + 30 + 42
 | = | 90 volts - Kirchhoff’s law is proved
V1 | = | I × R1
 | = | 6 × 3
 | = | 18V
Resistor 1
V2 | = | I × R2
Example 4

## Slide 13
The End
Unit 202: Principles of electrical science