## Slide 1
Power
Unit 202: Principles of electrical science

## Slide 2: Power
Power | = | Volts × Amps
Electrical power is the rate of doing electrical work or of expenditure of electrical energy.
The formula for Power is obtained by using the power triangle, as shown on the right.
From the triangle it can be seen that:
P | = | V.I (d.c. only)
or

## Slide 3: Power
P | = | I2R
Since Ohm’s law is: V = I × R, by substituting I × R for V in the power equation, we get: P = I × I × R giving:
(a.c. or d.c.)
P | = | V2 R
Since Ohm’s Law is: I = V/R, by substituting V/R for I in the power equation, we get: P = V/R × V giving:
(a.c. or d.c.)

## Slide 4
Example 1
Calculate the power in each resistance and the total power taken by the circuit.
Total power | = | V × I
 | = | 100 × 2
 | = | 200 watts
Power dissipated by R1 = P1:
P1 | = | I2R1
 | = | 22 × 30
 | = | 120 watts
Power dissipated by R2 = P2:
P2 | = | I2R2
 | = | 22 × 20
 | = | 80 watts

## Slide 5
Total power | = | P1 + P2
 | = | 120 + 80
 | = | 200 watts
Proving that when all the individuals powers in a circuit are added together, they will equal the total power in the circuit. This applies for both series and parallel circuits.
Example 1

## Slide 6
V | = | I × R
Alternatively, since:
 | = | 2 × 30
 | = | 60 volts
then voltage across R1 is V1:
V1 | = | I × R1
 | = | 120 watts
P1 | = | V12 | 
 |  | R1 | 
 | = | 602 | 
 |  | 30 | 
 | = | 120 watts
P1 | = | V1 × I | 
 | = | 60 × 2 | 
or
Example 1

## Slide 7
Similarly, voltage across R2 is V2:
 | = | 2 × 20
 | = | 40 volts
V2 | = | I × R2
 | = | 80 watts
P2 | = | V22 | 
 |  | R2 | 
 | = | 402 | 
 |  | 20 | 
 | = | 80 watts
P2 | = | V2 × I | 
 | = | 40 × 2 | 
or
Example 1

## Slide 8
The End
Unit 202: Principles of electrical science