## Slide 1
Generation of an EMF
Unit 202: Principles of electrical science

## Slide 2
Generation of an EMF

## Slide 3
EXAMPLE 1. A conductor of 15cm in length is moved at 20 metre/second (m/s) perpendicularly through a magnetic field of flux density 2 teslas. Calculate the induced EMF.
e | = | Blv
 | = | 2 × 0.15 × 20
 | = | 6 volts
Generation of an EMF

## Slide 4
EXAMPLE 2. A conductor of 0.5m in length is moved at 30 metre/second (m/s) perpendicularly through a magnetic field of flux density 3 teslas. Calculate the induced EMF.
e | = | Blv
 | = | 3 × 0.5 × 30
 | = | 45 volts
Generation of an EMF

## Slide 5
Fleming’s right hand generator rule
Direction of motion
Field
Current
Generation of an EMF

## Slide 6
Fleming’s right hand generator rule
Magnetic field goes this way from north to south
Conductor is moving upwards through the magnetic field
The current will flow towards us
Generation of an EMF

## Slide 7
The End
Unit 202: Principles of electrical science