## Slide 1
Basic mechanics
Unit 202: Principles of electrical science

## Slide 2
Basic mechanics
Mass
Mass can be defined as the amount of material in an object. The SI unit of mass is the kilogram (kg).
Acceleration
When an aircraft takes off, it starts from rest and increases its velocity until it can fly. This change in velocity is called acceleration. Acceleration is the change in velocity with time.
Acceleration | = | final velocity (v) - initial velocity(u) | (m/s2)
 |  | Time | 

## Slide 3
EXAMPLE 1. If a car accelerates from a velocity of 3 m/s to 15 m/s in 4 seconds, calculate its average acceleration.
Average velocity | = | 
Average velocity | = | 
Average acceleration | = | 
Average acceleration | = | 
 | = | 3m/s2
Average acceleration | = | 12 | 
 |  | 4 | 
Thus, the average acceleration is 3 metres per second, every second.
Basic mechanics

## Slide 4
Force
The SI unit of force is the Newton (N).
A mass of 1 kilogram experiences a force of 9.81 Newtons as a result of gravity. In other words, it would require a force of 9.81 Newtons to raise a mass of 1kg against the pull of gravity (on Earth).
To calculate the force on a body due to gravity (on earth) multiply its mass by 9.81.
Basic mechanics

## Slide 5
EXAMPLE 2. A bundle of conduit has a mass of 800kg. What force will be required to lift it?
Force required | = | Mass × Acceleration due to gravity
 | = | 800 × 9.81
 | = | 7,848 Newtons
Basic mechanics

## Slide 6
Work done
Basic mechanics
Force is measured in Newtons
Work done is measured in Newton metres (Nm)

## Slide 7
EXAMPLE 3. What work must be done to lift a 800kg bundle of conduit from the floor on to a rack 2 metres high?
Work done | = | Force x distance
 | = | 800 × 9.81 × 2
 | = | 15,696 Nm
Basic mechanics

## Slide 8
Energy
Energy is the capacity for doing work. It may exist in potential, kinetic, thermal, electrical, chemical, nuclear, or other various forms.
The units of energy is the Newton-metre or Joule.
Basic mechanics

## Slide 9
Power
POWER is defined as THE RATE OF DOING WORK.
Basic mechanics
 | The unit of Power is the watt. | Since the watt is a small unit, the kilowatt is often used. | 
 | The unit of Power is the watt. | Since the watt is a small unit, the kilowatt is often used. | 

## Slide 10
Efficiency
The efficiency of a system can be defined as the ratio of output power to input power and is usually expressed as a percentage.
Basic mechanics

## Slide 11
EXAMPLE 4. A motor produces 100 watts output power and is:
50% efficient
70% efficient.
Calculate its input power in each case.
 | Efficiency | = | Output power | × 100
 |  |  | Input power | 
 | = | 200 watts
 | Input power | = | Output power | × 100
 |  |  | Efficiency | 
a) | Input power | = | 100 | × 100
 |  |  | 50 | 
Basic mechanics

## Slide 12
 | = | 142.86 watts
 | Input power | = | Output power | × 100
 |  |  | Efficiency | 
b) | Input power | = | 100 | × 100
 |  |  | 70 | 
Basic mechanics

## Slide 13
EXAMPLE 5. An electric motor drives a pump that lifts 1,000 litres of water each minute to a tank 20 metres above ground level. Calculate the power that the motor must provide if the pump is only:
50% efficient
80% efficient.
Work | = | Force × distance
Force | = | Mass in kg × 9.81
 | = | 1,000 × 9.81 × 20
 | = | 196,200Nm/minute or joules
Joules | = | Watts × seconds
 | Watts | = | Joules | 
 |  |  | seconds | 
 |  | = | 196,200 | 
 |  |  | 60 | 
 | = | 3,270 Watts (output power)
NB: One litre of water weighs 1kg (1kg = 9.81N)
Basic mechanics

## Slide 14
 | Efficiency | = | Output power | × 100
 |  |  | Input power | 
 | = | 6,540 watts
 | Input power | = | Output power | × 100
 |  |  | Efficiency | 
a) | Input power | = | 3,270 | × 100
 |  |  | 50 | 
Basic mechanics

## Slide 15
 | = | 4,087.5 watts
 | Input power | = | Output power | × 100
 |  |  | Efficiency | 
b) | Input power | = | 3,270 | × 100
 |  |  | 80 | 
Basic mechanics

## Slide 16
The End
Unit 202: Principles of electrical science