## Slide 1
Wiring systems
Unit 203: Electrical installations technology

## Slide 2
Environments:
domestic installations
commercial installation
hazardous installations
industrial installations
agricultural installations.
Wiring systems

## Slide 3
Clipped direct:
Mineral insulated (MICC)
Steel wired armoured (SWA)
Cross-linked polyethylene (XLPE)
Polyvinyl chloride/polyvinyl chloride (PVC/PVC).
Wiring systems

## Slide 4
Steel conduit and trunking:
generally used to deliver single core cables in industrial, commercial and health settings
strong and able to resist high mechanical stresses.
Wiring systems

## Slide 5
Plastic conduit and trunking:
as with steel conduit and trunking, single core cables are generally installed in schools and commercial premises.
less robust than steel conduit but easier to install.
Wiring systems

## Slide 6
Cable tray:
commonly used to support a number of cables where individual clipping is difficult or not economical.
tray is used either above ceilings or in industrial or commercial settings.
it has a range of sizes from 50mm to 1,000mm.
Wiring systems

## Slide 7
Ladder rack:
similar to cable tray but with greater strength and used in industrial settings to deliver large numbers of sub-main cables.
Wiring systems

## Slide 8
Basket tray:
similar to cable tray but more likely to be used in commercial premises for large amounts of smaller cables.
Wiring systems

## Slide 9
The End
Unit 203: Electrical installations technology