## Slide 1
Fire resistant cables
Unit 203: Electrical installations technology

## Slide 2
Two types of cable are available for this purpose:
mineral insulated copper clad (MICC)
FP200.
Fire resistant cables

## Slide 3
Mineral insulated copper clad (MICC) cable
Advantages:
fireproof
great mechanical strength
waterproof
non-ageing
small overall diameter
high current carrying capacity
earth continuity
high corrosion resistance
high operating temperature.
Disadvantages:
moisture absorption
complicated termination process
cost.
Fire resistant cables

## Slide 4
FP200
Conductor
cpc
Insulation
Screen
Sheath
Fire resistant cables
Advantages:
fire resistant
good mechanical strength
waterproof
easy to terminate
relatively cheap compared to MICC.
Disadvantage:
types with silicon insulation require ferrules to be fitted because this insulation is brittle and easily damaged.

## Slide 5
The End
Unit 203: Electrical installations technology